## Slide 1
Chapter 18 Electrolytes
Strong Electrolyte NaCl in water (strong dielectric, ions completely formed)
Weak Electrolyte Acetic Acid in water (use dissociation constant)

## Slide 2
Chapter 18 Electrolytes
Handbook of Aqueous Electrolyte Thermodynamics

## Slide 3
Colligative (counting) Properties
Melting Point Depression
Osmotic Pressure P/RT = (c/Mw) (1 + B2 c + …)
Boiling Point Elevation (for non-volatile solute)
yH2O P = P = xH2OPH20Sat

## Slide 7
Speciation and dissociation constant Ka,298, charge balance
aH+ is dimensionless, [H+] is moles/liter (molarity, MH+)
A neutral solution is pure water so aH2O = 1
With temperature changes [H+] changes due to thermal expansion
Molality, number of moles of H+ per kg of H2O is used, mH+

## Slide 9
Concentration with speciation
Acetic Acid in water
Apparent concentration: g/liter you put in of C2H4O2
True concentration has to do with the dissociation species (based on a model)
VLE is based on the true concentration of undissociated species

## Slide 10
pH
pH = -log10(aH+)
aH+ is molal (molar as an approximation)

## Slide 11
Electrolyte Equilibrium Constant
Succinic Acid

## Slide 12
Water of hydration and hydronium ion
Cations have water of hydration associated with the ion
Degree of hydration changes with concentration
At high concentrations ion pairs with the counter ion form

## Slide 13
Acids and conjugate bases

## Slide 14
Strong Acid
[H+] is large so [OH-] is very small, can be ignored
pH ~ pCA

## Slide 15
Strong Base
[OH-] is large so [H+] is very small, can be ignored
pOH ~ pCB

## Slide 16
Weak monoprotic Acid (Acetic Acid pKa,A = 4.7)

## Slide 17
Weak monoprotic Based (Acetate ion pKa,B = 9.3)
Start with sodium acetate which is a strong electrolyte, the resulting acetate ion is a weak base
Convert to an acid equation and work with weak acid

## Slide 18
Acid or Base Added to water

## Slide 19
Acid
Base
Standard acid form of eqn. 18.38
At 298K, Ka,B = 6.18 e-13 from eqn. 18.39
Ka,A = 1e-14/6.18e-13 = 0.0162 or pKa,A = 1.79
Fluconazole is protonated below pH = 1.8 and neutral (undissociated) above
pH = 7
None is dissociated so:

## Slide 20
Acid
Base
Standard acid form of eqn. 18.39
At 298K, Ka,B = 6.18 e-13 from eqn. 18.39
Ka,A = 1e-14/6.18 e-13 = 0.0162 or pKa,A = 1.79
Fluconazole is protonated below pH = 1.8 and neutral (undissociated) above
pH = 1.5
About half is dissociated:

## Slide 21
Sillén Diagram or Bjerrum Plot or Hägg Diagram
4.76 = pKa

## Slide 22
Sillén Diagram

## Slide 25
When [OAc-] = [HOAc] then Ka,A = [H+]
When one component is small the other is CB
Strong Base/Weak Acid, Answer is Basic
In Basic region [H+] << [HOAc]
So [HOAc] ~ [OH-] for solution at pH 8.4
[HOAc] is parallel to [H+] when [H+] is small
[H+]=10-14/[OH-] so [OAc-] is parallel to [OH-] when [OH-] is small
[OH-][H+]=10-14 so log [OH-]+log[H+] = 14 (two lines as drawn)

## Slide 34
Amino Acids (Zwiterions)

## Slide 35
Amino Acids (Zwiterions)

## Slide 37
Charge balance (18.67) is reached about where 1.1[H2Gly+] = [Gly-], a little above pH = 6

## Slide 38
Buffer: a salt and an acid that share a common ion
Acetic Acid and Sodium Acetate
Henderson-Hasselbalch Equation

## Slide 39
Buffer: a salt and an acid that share a common ion
Acetic Acid and Sodium Acetate
Better equation:

## Slide 40
Isoelectric Point
For a zwitterion like an amino acid amines protonate at neutral pH and carboxylic acids are deprotonated. When there is no net charge the pH = pI is the isoelectric point. Solubility is at a minimum at the isoelectric point.

## Slide 41
Ionic Strength (salt concentration)
For low ionic strength, as ionic strength increases, solubility increases (salting in).
For high ionic strength, as ionic strength increases, solubility decreases (salting out).
Maximum solubility at intermediate salt concentrations.
Salting in

## Slide 42
Donnan Equilibria

## Slide 43
Solubility
Solubility and vapor pressure rely on equilibria with the un-ionized species. So solubility depends on pH. Remember, the activity of a solid is 1.
KSLE = 0.0180 at 298K; pH 1.5 [H+] = 0.0316; pH 7 [H+] = 1e-7; Ka = 6.18 e-13; pKa = 1.8 so protonated below pH 1.8 and undissociated above pH 7
From slide 18 example 18.4

## Slide 44
Common ion effect
Add NaCl to a KCl saturated solution causes precipitation

## Slide 45
Redox Reactions OILRIG
Lose or gain electrons
Electrochemical Cell (discharge)
Anode:
Cathode:
3.9 Volts
Oxidation (OIL)
Reduction (RIG)
Reference voltage is platinum electrode:H2(g) electrode at pH = 0; 298K; 1 bar
Reduction of H+ Potential set to 0 as reference

## Slide 47
Redox Reactions OILRIG

## Slide 51
Bioprocess Engineering (Fermentation)
Degree of Reduction
Stoichiometry
Oxidation State
O2 is 0; in products is -2
Moles of electrons transferred to oxygen
The degree of reduction multipliers are +4 for C; +1 for H; -2 for O; -3 for N (ammonia); +6 for S (H2SO4); +5 for P (phosphoric acid)
Reaction of acetaldehyde C2H4O Degree of reduction 2(4)+4(1)+1(-2)=10 or 5 per carbon.
To determine r for O2, 2r(-2) = -10 so r = -2.5 to yield zero on the left of 18.88
On the right of 18.88, For CO2, 1(4)+2(-2) = 0 and for H2O, 2(1)+1(-2) = 0
Two sides balance

## Slide 53
Biological Equilibrium Reactions
Reactions occur with a buffer so [H+] is ignored (indicated by prime)
Water is pure so activity is 1

## Slide 58
Debye-Hückel Model
Mean field

## Slide 59
Debye-Hückel Model
Coulomb’s Law
Work to place an ion in a solution of other ions

## Slide 60
Debye-Hückel Model

## Slide 61
Activity Coefficient of Water
Can be determined by measuring the osmotic pressure

## Slide 62
Chlorination of Water

## Slide 65
Double [H+] makes it about 0.3 higher

## Slide 66
Double [H+] makes it about 0.3 higher

## Slide 68
Mean (Geometric Mean) Ionic Activity Coefficients
Mean Molality:
Mean Ionic Activity Coefficient:
Stoichiometric Number