## Slide 1: Instructions for configuring Windows XP Professional Service Pack 2 to work with ASTRA V
Wyatt Technology Corporation
Santa Barbara, CA

## Slide 2: Notes:
It is necessary to follow these instructions if you wish to use ASTRA V to do any of the following:
  Collect data from an HELEOS, TREOS, Optilab rEX or ViscoStar.
  Connect to an ISI on another networked computer.
If you are only going to use ASTRA V for data processing, or to collect data from a DAWN, miniDAWN, or WyattQELS, it is not necessary to follow these instructions.
Administrator or Power User privileges may be required to configure Windows XP Professional.

## Slide 3: Modifying COM settings
Step 1: From the Start menu, choose Control Panel.

## Slide 4: Modifying COM settings
Step 2: In the Control Panel, open the Administrative Tools.

## Slide 5: Modifying COM settings
Step 3: From Administrative Tools, open the Component Services Shortcut.

## Slide 6: Modifying COM settings
Step 4: In the Component Services dialog, expand the tree on the left down to the level Console Root | Component Services | Computers | My Computer.

## Slide 7: Modifying COM settings
Step 5: Right click on My Computer and select Properties.

## Slide 8: Modifying COM settings
Step 6: In the Properties dialog, select the COM Security tab, then select Edit Limits… under Access Permissions.

## Slide 9: Modifying COM settings
Step 7: In the Access Permissions dialog, choose ANONYMOUS LOGON under Group or user names, then check the Allow box for Remote Access under Permissions. Click OK, then click Apply in the Properties dialog.

## Slide 10: Modifying COM settings
Step 8: In the Properties dialog, select the COM Security tab, then select Edit Limits… under Launch and Activation Permissions.

## Slide 11: Modifying COM settings
Step 9: In the Launch Permissions dialog, choose Everyone under Group or user names, then check the Allow box for Remote Launch and Remote Activation under Permissions. Click OK, then click Apply in the Properties dialog.

## Slide 12: Conclusion
Your computer should now be configured to collect data from an HELEOS, TREOS, Optilab rEX, ViscoStar, or remote ISI.
If you still have problems collecting data from these instruments, please see the Appendix for a detailed matrix of all the COM settings.

## Slide 13: Appendix: Complete COM Settings

## Slide 14: Setting Network rankings
Network performance can be improved by ranking multiple networks if they
exist. Lab computers may be connected to a corporate network, and more
Than one instrument LAN. Ranking the order that Windows searches for
Network locations can improve overall performance. Start by opening
the Network Connections dialog box (in Control Panel)

## Slide 15: Networking Ranking (continued)
From the main toolbar, select Advanced, Advanced Settings

## Slide 16: Networking Ranking, continued
The main network connection to the corporate network should be the top entry in the list. If it is not the first entry, you can highlight it and use the green up arrow key to move it to the top entry

## Slide 17: Adding static IP Address information to HOSTS file
You can speed up ASTRA connections by adding the name
and IP address of ethernet-based detectors to the Windows
HOSTS file. This includes the HELEOS, TREOS,
Optilab rEX, and Viscostar.
This may also help remove and prevent detector entries in
ASTRA that show a red “X”.
Instruments with serial communications (EOS, miniDAWN
Tristar, and earlier) do not need to be added to the list.

## Slide 18: Open the Windows HOSTS file
Use Windows Notepad accessory to edit the HOSTS File. Notepad works better than Wordpad or other Word processing software since the HOSTS file has no file extension; Word or Wordpad will try to add a *.txt extension to the file.
Pathway to HOSTS file: C:\WINDOWS\system32\drivers\etc

## Slide 19: Add Detector name and IP address to HOSTS list
This list shows the addition of an Optilab rEX with IP address 192.168.254.100 and computer name wyatt-123-rex. The computer name can be found on the communications tab on the detector front panel. Save the file after adding the information; add each detector as a separate entry.