## Slide 1
Light Scattering University
Wyatt Technology Corporation
Santa Barbara, California
Introduction to ASTRA 6
Notes: Talking points are suggested in this section.

## Slide 2: Overview
Practical:
  Software installation and activation
  Connecting to instruments
  Running the “first” experiment – a toluene calibration
Presentation:
  Architecture & Compliance
  Experiments, Methods, Configurations
  Data Collection: Single Experiments or Sequences
Notes: This is a two-part workshop.

## Slide 3: Flexible Configuration, Fully Networked
ASTRA 6
Optilab or
3rd party RI
WyattQELS
UV
ViscoStar
DAWN or miniDAWN
Notes: Let us know if you would like to import other data types for analysis in ASTRA!

## Slide 4: Three Tiers
Basic
With Research Database
Security Pack
(21 CFR Part 11 Compliant)
Notes: As of August 2011, ASTRA 6 does not yet support the Research Database or Security Pack tiers.
Please, it’s “Tiers” not “Tears!”

## Slide 5: Experiments
Hardware setup, processing, and results are grouped together as an experiment.
After collection, raw data is stored and locked within the experiment.
ASTRA’s “Experiments” view captures the logical construction and flow of an experiment.
- This view is the most common selection for the left-hand side of your ASTRA window.
Notes: You can never “hurt” your raw data after collection, as you work with an experiment. You can always start over with your analysis by deleting your processing parameters or applying a method.
Custom graphs and reports are a nice touch! To be covered in a later session…

## Slide 6: Configurations
Hardware constants & settings are stored in profiles, which are grouped into Configurations.
Notes: You create individual profiles for custom solvents and other new entities.

## Slide 7: Methods
Experiments are generated from a method.
A comprehensive set of system methods is provided. ♥
- These system methods need to be personalized before collection.
The wizard is an easy way to generate & personalize your first method.
Experiment method

## Slide 8: Configurations
Replacing a Configuration (right-click Configuration and select Replace Configuration) may be necessary to correct or update system constants after data collection.
The “One-to-Many” tool is a convenient means for updating system constants in multiple experiments.
Notes: Replacing a configuration is a relatively rare procedure, such as if the wrong method was used for collection or if the normalization run was part of the sequence itself. This is how you change the top portion of an experiment.

## Slide 9: Applying a Method
Applying a method to a collected experiment
  will change processing procedures / results
  will not affect configuration or existing baseline/peak settings!
Certain ASTRA methods have been provided for advanced processing. ♥
A list and description of all available methods is available in the ASTRA 6 Software User Guide
Experiment method
Notes: Applying a method is relatively common. It’s how we do many of the advanced processing techniques in ASTRA. This is how we change the bottom portion of an experiment.

## Slide 10: Recap
Experiments combine configuration, procedures, results, and data.
Experiment Methods can be used to collect or re-analyze data.
Configurations store hardware settings and detector constants.

## Slide 11: Data Collection
Single experiments, manual or single injection with an autosampler
Sequences, autosampler injections
Collection techniques:

## Slide 12: Single Experiments
Create a new experiment using the Configuration Wizard or manually from a system method.
Run the experiment.
Data from single collection is stored with the experiment.
Results are generated automatically if the method includes processing info, or user will be prompted for processing information (i.e. set baselines, peak settings, missing dn/dc).

## Slide 13: Sequences
Sequences contain pointers to one or more method to be run sequentially.
As the sequence is run, a new experiment is created for each sample injection.
sequence
Experiment method

## Slide 14: Sequences
It is possible to use a different method for each sample.
Experiment types can be varied on an injection by injection basis.
Sample sets from Waters Empower software can be imported directly into ASTRA or sequences can be set up manually.
sequence
Experiment method 1
Experiment method 2
Experiment method 3

## Slide 15: Next…
Software installation and activation
Connecting to instruments
Running a first experiment: Light Scattering Instrument Calibration with Toluene

## Slide 16: Appendix: Terminology & Units ASTRA V versus ASTRA 6
Terminology Changes | ASTRA 6 | ASTRA V
 | Method | Template
 | Sequence | Sample Set
Notes: For the seasoned ASTRA V user…